## Slide 1
Energy efficient Architecture for 5G network:
A crucial goal of 5G network is to create an energy efficient infrastructure. There are different ways of creating energy efficient infrastructure.
Depending on the load, channel conditions, services and applications requirements, a user centric 5G network can be used for selecting UL and DL channels from different BSs. Decoupling signal and data are useful. When there is no data traffic in SBS, it can be turned off.
If an UE connected with SBS following the instructions by a MBS ,it can be less energy consumption at UEs for less interference. Also quick small cell discovery and MBS-assisted handover.
A C-RAN architecture can be energy efficient where it can be serve almost a same numbers of UEs. It provides an interference management approach causing less energy consumption of SBSs & MBSs.
Association of a UE can only be done considering both UL and Dl channel.
Also we can use an energy harvesting device(e.g. Thermoelectric Generator) and a spectrum harvesting controller(Quantum Dot Solar Cell) at SBSs.
Interference Management in 5G Networks:
An advanced receiver which detects, decodes and removes interference from receiving signals.
Network side interference can be managed by a joint scheduling, selects each UE according to resources (e.g. time, frequency, transmission rate and schemes of multiple cells) which associated with a BS. It requires a coordination mechanism among the neighboring cells.

## Slide 2
  CAPC schemes can be used for handling interference in multi-tier architecture. It involves i) prioritized power control(PPC) SBSs have lower priority than working under a MBS ii) cell association(CA) including dynamic values of resources, traffic, distance to MBS iii) resource-aware CA & PPC combines the first two approaches allows a UE simultaneously connect with multiple BSs for UL and DL according to criteria of PPC and CA.
  Self-interferences cancellation(SIC) in small cells networks requires methods to transfer backhaul data to a MBS. Use of SIC eliminate such methods and caused SSCs.
  A small cell completely remove the need of a separate backhaul data transfer method causing reduced cost.
  Allocation of UL & DL channels by MBS can tolerate inter-user UL to Dl interference in a single-cell full duplex radio network.
Open issue:
  Design of algorithms for interference cancellation in a full duplex radio network is still open & needed to be explored.
Handoff Management in 5G Network:
A way to connect to a UEs to BS to move to another BS without disconnecting.
Challenges:
  Improved routing
  Security
  Certainty of having services
  Densification
  Very high mobility
  Zero latency
  Accessing multi-RATs
  Efficient load balancing

## Slide 3
Types:
  Intra macro cell handoff: Handoff between small cells working for a single MBS.
  Inter macro cell : handoff between macro cells.
  Multi-RATs handoff: handoff of UEs from a RAT to other RAT.
Prevention:
  For highly mobile users measuring report to current MBS.
  For handoff between RATs, UE can select the most suitable RATs without any performance loss.
Open Issues:
  Yet to be explored.
  Developed algorithm for different types of interference.
  Tradeoff between number of handoffs and level of interference.